## Slide 1: Nuclear Magnetism and NMR Spectroscopy
Nuclear Magnetic Resonance – Theory and Techniques
Ralph W. Adams
ralph.adams@manchester.ac.uk

## Slide 2
Introduction to this course
Part 1 will cover the basics of NMR theory
Part 2 will introduce and discuss the wide range of NMR methods available
Part 3 will provide several workshops, applying the knowledge introduced in the lectures
The course expands on courses run by Tim Claridge at The University of Oxford, Abil Aliev at University College London, and James Keeler at The University of Cambridge.
Much of the material will be taken from the texts Nuclear Magnetic Resonance (2e) by Peter J. Hore (Oxford Chemistry Primer) and High Resolution NMR Techniques in Organic Chemistry (3e) by Tim D. W. Claridge (Elsevier) which provide a more complete introduction to NMR spectroscopy.
Only liquid state NMR will be discussed

## Slide 3: Nuclear Magnetism and NMR Spectroscopy
History
Spin angular momentum
Magnetic moments
Energy levels
Resonance frequencies and chemical shift
Populations and polarization

## Slide 4: Some NMR history
1926 – Prediction of nuclear spin (Pauli)
1932 – Detection of nuclear magnetic moment (Stern)
1945 – NMR spectra of solution (Bloch*) and solids (Purcell*)
1949 – Discovery of chemical shift
1964 – Pulse FT NMR (Ernst* and Anderson)
1971 – 2D NMR experiment proposed (Jeener)
1972 – MRI Image collected (Lauterbur*)
1974 – 2D NMR demonstrated (Ernst)
1979 – 2D NOESY
1980 – NMR protein structure (Wuthrich*)
*Nobel prizes awarded in physics, chemistry (x 2) and medicine.

## Slide 5: Spin angular momentum
spin is an intrinsic property of magnetic nuclei
The magnitude of spin angular momentum is ħ.
I | Nuclide
0 | 12C, 16O
1/2 | 1H, 13C, 15N, 29Si, 31P
1 | 2H, 14N
3/2 | 11B, 23Na, 35Cl, 37Cl
5/2 | 17O, 27Al
3 | 10B

## Slide 6
Spin angular momentum

## Slide 7
Spin angular momentum
The Stern-Gerlach experiment confirms spin and quantization

## Slide 8
Magnetic moments
Spin angular momentum can be described using a vector I whose direction and magnitude are quantized.
The length of I is ħ with 2I + 1 projections along the axis of the applied magnetic field.
The magnetic moment µ is related to the spin angular momentum I by µ = γ I where γ is the magnetogyric ratio of the nuclide.

## Slide 9
Nuclide | γ ( 106 rad s−1 T−1) | ν (MHz T−1)
1H | 267.513 | - 42.58
2H | 41.065 | - 6.54
13C | 67.262 | - 10.71
15N | −27.116 | 4.32
19F | 251.662 | - 40.05
29Si | −53.190 | 8.47
31P | 108.291 | - 17.24
Magnetic moments
How do you convert from γ to ν?
What are the NMR frequencies of 1H and 13C at 9.4 T and 23.5 T?

## Slide 10
Energy levels
For strong magnetic fields the spins are quantized along the axis of the magnetic field.
The energy E of a spin is the product of the z-component of the magnetic moment µz and the magnetic field B.
µz = γ Iz = γ m ħ
E = - γ m ħ B.
Label the figure to give the energy for each value of m for I = 1

## Slide 11: A common misconception

## Slide 12: A common misconception – corrected

## Slide 13
NMR spectroscopy
νNMR is in the radiofrequency part of the electromagnetic spectrum so we use the term R.F. field when discussing the radiation required to irradiate NMR transitions.
an appropriate radio- frequency is applied to rotate the bulk magnetisation vector into the transverse plane
Larmor precession is then observed and used to generate an NMR signal

## Slide 14
NMR spectroscopy

## Slide 15
NMR spectroscopy
Angular momentum, resonance and precession can be demonstrated using a gyroscope.

## Slide 16
Populations and polarization
The populations of energy levels in NMR spectroscopy can be calculated using nβ / nα = exp(-ΔE / kBT)
With ΔE = γ ħ B = 2.65 x 10-25 J and kBT = 4.14 x 10-21 J
ΔE/kBT = 6.4 x 10-5
The available thermal energy, kBT, is large compared to the energy required to reorient the spins and that the population difference will be small.
nα = 15625
nβ = 15624
Population difference is only 1 in 31250 molecules so NMR signals will be very weak.

## Slide 17: Nuclear Magnetism and NMR Spectroscopy
Nuclear Magnetic Resonance – Theory and Techniques
Ralph W. Adams
ralph.adams@manchester.ac.uk