## Slide 1: 2D J-Spectroscopy and DOSY
Nuclear Magnetic Resonance – Theory and Techniques
Ralph W. Adams
ralph.adams@manchester.ac.uk

## Slide 2: Introducing 2D J-Spectroscopy
Rather than using scalar (J) couplings to correlate signals, here we aim to separate them from chemical shift

## Slide 3: Heteronuclear J-resolved Spectroscopy
In the heteronuclear version of the J-resolved experiment, the chemical shift of the X spin is presented in f2 while couplings to a second nucleus, typically protons, are presented in f1.
The f1 dimension therefore enables an analysis of resonance multiplicity as well as measurement of heteronuclear-coupling constants (JXH).

## Slide 5: Measuring Long-Range Proton–Carbon Coupling Constants
Long-range 1H–13C coupling constants can be used to define molecular configuration or conformation
J-resolved methods are well suited to such measurements, but suffer from the presence of the far greater 1JCH couplings
If less informative one-bond 1H–13C couplings are suppressed from f1 spectral width can be reduced and higher resolution can be achieved
1JCH values are greater than c. 125 Hz, while long-range couplings are typically less than 10 Hz

## Slide 6
13C detected

## Slide 7
1H detected - The H1’ proton has been selectively inverted, and the doublet splittings in f1 record its long-range couplings to C8 and C2’.

## Slide 8: Homonuclear J-resolved Spectroscopy
The homonuclear version of the J-resolved experiment is most frequently applied in proton spectroscopy, although it is suitable for any abundant nuclide.
The separation of δ and J should reveal proton multiplets in f1, and singlets in f2 at the corresponding chemical shifts, such that the f2 projection represents the ‘broadband proton-decoupled proton spectrum’.
Generates ‘pure shift’ spectrum and allows measurement of homonuclear-coupling constants.

## Slide 9
The homonuclear sequence closely resembles the heteronuclear methods
The appearance of the homonuclear spectrum is different from its heteronuclear equivalent in that both chemical shifts and couplings appear in f2.
Multiplets appear at 45 degrees to either axis.
Columns parallel to f1 do not display the expected proton multiplets, and the f2 projection displays both chemical shifts and scalar couplings.

## Slide 10: Processing
To reach the ultimate goal of retaining only chemical shifts in f2, it is possible to eliminate the couplings from by ‘tilting’ the multiplets through an angle of 45 degrees about their midpoints.
The resulting spectrum then has an appearance similar to the heteronuclear analogue, with columns parallel to f1 reproducing the multiplet structures.
Magnitude calculation must be performed so signals will have their amplitudes and shapes distorted.
If the whole data set is symmetrised about f1 = 0 the multiplets are retained whereas contributions from the sloping t1 noise and other spectral impurities are diminished.

## Slide 11
(a) The 2D J spectrum after tilting and symmetrisation. The f2 projection (b) approximates to the ‘proton-decoupled proton spectrum’ and is considerably less complex than the conventional 1D spectrum (c). 4K t2 data points were acquired for 64 t1 increments over spectral widths of 5 ppm and 60 Hz, respectively. The final f1 resolution after zero-filling was 0.5 Hz/pt. Data were processed with unshifted sine bell windows in both dimensions and are presented in magnitude mode

## Slide 12
(a) Selected f1 traces taken from a J-resolved spectrum and (b) equivalent multiplets from the 1D proton spectrum.

## Slide 14: Introducing DOSY
Rather than correlating spins with each other, we measure their change in position over time to determine how the molecule to which the spin is attached diffuses in the solution.
Diffusion coefficients can then be used to infer information about the molecules.

## Slide 15
PFGSTE spectra are measured as a function of G.
By fitting peak heights to the Stejskal-Tanner equation diffusion coefficients, D, are obtained.
1D peaks are extended into a second dimension, with Gaussian shapes centred on the D’s and widths determined by the standard errors σD.
400 MHz 1H DOSY spectrum of choline,
acetone and DSS in D2O
DSS
Choline
Acetone
HDO
G
Constructing a 2D DOSY spectrum

## Slide 16
nmr.chemistry.manchester.ac.uk
Strengths of greatest and smallest diffusion gradient levels
Diffusion gradient pulse width
Number of gradient levels
Diffusion time
How do we acquire a DOSY spectrum?
Appropriate parameter settings
Pulse calibration
Recycle time
Acquisition time, etc

## Slide 17
nmr.chemistry.manchester.ac.uk
Optimising parameter settings
S1
e
S1
Good fitting to the Stejskal-Tanner equation can normally be achieved if the signals in the spectrum with most attenuation have intensity ≈1/e of those in the spectrum with least attenuation.
Acquiring the spectra with the greatest and smallest gradient levels from the full DOSY series, with a reduced number of transients, allows parameters to be appropriately set.

## Slide 18
nmr.chemistry.manchester.ac.uk
Optimising parameter settings
S1
e
S1
Diffusion time
Strengths of strongest and weakest diffusion gradient levels
Diffusion gradient pulse width
Number of gradient levels
Choose Δ short compared to T1.
Set to highest available for the strongest level and lowest available for weakest level (while maintaining CTP if using Oneshot type sequences).
Adjust value to get desired signal attenuation.
For mono-exponential fitting choose 10.

## Slide 19
nmr.chemistry.manchester.ac.uk
Acquire the DOSY
DOSY spectrum
DOSY spectra should be acquired with the gradient strength incremented in steps of gradient2.
Signal attenuation in a DOSY experiment
D / x10-10 m2 s-1

## Slide 20
nmr.chemistry.manchester.ac.uk
Phase dependence on gradient strength
In addition to the desired signal attenuation, there is often a phase change that results from the change in gradient strength.
The phase change can usually be reduced by increasing the gradient stabilisation delay (gstab/d16).
Use of reference deconvolution can completely remove the effects of phase change.
Signal phase in a DOSY experiment

## Slide 21
Experimental NMR Spectrum
Experimental FID
Experimental Ref. FID
Ideal Ref. FID
Reference Deconvoluted NMR Spectrum
Synthetic
Reference
Peak
IFT
IFT
C
=
Reference Deconvoluted FID
FT
C =
Reference Deconvolution

## Slide 22
nmr.chemistry.manchester.ac.uk
Reference Deconvolution
Reference
Deconvolution
Resolution enhancement
Frequency correction
Phase correction
Benefits for DOSY data
Singlet (TSP)
Adequate amplitude in all spectra
Requirements

## Slide 23
Reference Deconvolution

## Slide 24
Chemical Exchange
Exchange during the diffusion delay of the Oneshot45 stimulated echo leads to averaging of diffusion coefficients.
Exchange in PROJECTED (PROJECT Extended for DOSY) leads only to signal loss, not to diffusion averaging, because the magnetization remains transverse during the diffusion delay.
OH H2O exchange in hesperidin in dmso-d6
nmr.chemistry.manchester.ac.uk

## Slide 25: 2D J-Spectroscopy and DOSY
Nuclear Magnetic Resonance – Theory and Techniques
Ralph W. Adams
ralph.adams@manchester.ac.uk